## Slide 1: How to Approach Breast Ultrasound
Mai Elezaby1, MD
Cecelia Marcado2, MD
Monica Sheth3, MD
University of Wisconsin School of Medicine and Public Health
NYU Langone Health
NYU Langone Health

## Slide 2: Indications
Patients present for breast ultrasound for either screening or diagnostic purposes
Screening:
Asymptomatic patients with high risk for breast cancer and contraindication to screening MRI
Asymptomatic patients with dense breast (ACR categories C or D) +/- ↑ risk of breast cancer
Diagnostic-Problem Solving for the evaluation of:
Breast symptoms: lump, pain, nipple discharge, skin retraction
  Patients < 30 years, US first, otherwise start with MG
Mammographic abnormality
MRI abnormality

## Slide 3: Equipment
Linear Transducer
Hockey stick transducer
Monitor
Keyboard to control imaging settings and label images
Standard US Equipment:
Monitor - displays images
Keyboard - houses controls to optimize images - focal zone, depth, spatial compounding, gain, harmonics, etc. to clarify images
Measurement tools and doppler imaging to provide additional details.
Transducers - come in various frequencies
  lower frequency transducers having deeper penetration of tissue.

## Slide 4: Technique: Optimize Imaging
High frequency, linear array transducer
  with center of frequency of at least 10MHz
  with maximum frequency 12-18 MHz
Field of view - reach chest wall but not beyond
Overall gain - set so that fat is gray
TGC - increase with increasing depth
Focal zone - set at lesion
  Most transducers allow for multiple focal zones
  Increase resolution of lesion with one focal zone
Focal Zone

## Slide 5: Technique: Patient Positioning
Positioning is key to immobilize breast tissue and aid with scanning
Good positioning includes:
  Arm above the head - helps thin and spread breast tissue for improved penetration
  Lying supine to evaluate medial tissue
  Lying supine oblique for lateral breast and axilla evaluation
  Wedges can be used to provide additional support

## Slide 6: Approach: Scanning planes
Document findings in two planes (transverse/longitudinal or radial/antiradial). Images below demonstrate orientation of the transducer (blue rectangle) in relation to the breast
Anti-radial - perpendicular to radial spokes
Transverse
Longitudinal
Radial- spokes on wheel

## Slide 7: Lesion Location:
Findings in ultrasound are given two location identifiers:
1) Clock face position 2) Distance (cm) from the nipple ssssssssssssssssssssssssssssssssssssssssss(center of probe to nipple)

## Slide 8: Lesion Location:
Now let’s practice. What is the clock face position of the following findings?
Right Breast:
Left Breast:
Right
Left
2:00
7:00

## Slide 9: Normal Anatomy
Skin
*Fat - hypoechoic (gray)
Fibroglandular tissue - echogenic (light gray/white)
Skeletal muscle
(Pectoralis muscle/chest wall)
Ribs
Lung Pleura
Important to note that echogenicity of ultrasound findings are described relative to echogenicity of breast fat.

## Slide 10: Relationship of tissue depth on MG and US
Closer to skin
Within
Glandular tissue
Closer to pectoralis muscle

## Slide 11: Ultrasound Reporting: BIRADS
https://www.acr.org/~/media/ACR/Documents/PDF/QualitySafety/Resources/BIRADS/Posters/BIRADS-Poster_36x24in_F.pdf?la=en

## Slide 12
Tissue Composition
(Screening Ultrasound)
Homogeneous background
echotexture - fat
Heterogeneous background echotexture
Homogeneous background echotexture - fibroglandular
On screening ultrasound exams, documentation of the patient’s tissue background echotexture is a standard component of report.

## Slide 13
Ultrasound Findings
Mass - Shape
Oval
Round
Irregular
Lower likelihood of malignancy (LOM)
Higher LOM

## Slide 14
Ultrasound Findings
Mass - Margin
Circumscribed
Spiculated
Microlobulated
Indistinct
Angular
More suspicious

## Slide 15
Ultrasound Findings
Mass - Echogenicity
Anechoic
Hypoechoic
Hyperechoic
Brighter than FAT (light gray-white)
Usually benign
No internal echoes (black)
Mostly indicates simple cyst
Darker than FAT
Most of masses

## Slide 16
Ultrasound Findings
Mass - Echogenicity
Isoechoic
Complex Solid and cystic
Heterogeneous
Similar to FAT
Typically benign
Highly suspicious for malignancy

## Slide 17
Ultrasound Findings
Mass - Orientation
More common with benign masses
More common with malignant masses
wider than tall
Taller than wide

## Slide 18
Ultrasound Findings
Mass - Posterior Features
Tissue posterior to mass is brighter
Tissue posterior to mass is darker
None
Shadowing
Enhancement
Combined

## Slide 19: MASS SUMMARY
More common with Benign | More common with Malignant
Oval | Round/irregular
Circumscribed | Not circumscribed (indistinct, microlobulated, angular, spiculated)
Posterior enhancement | Posterior shadowing
Hyperechoic/isoechoic | Hypoechoic
Parallel | Not-parallel

## Slide 20: CYSTS
MLO
CC
Simple Cyst
Anechoic
Smooth internal wall
Posterior enhancement
No internal vascularity
Benign-No follow up needed

## Slide 21: CYSTS
MLO
CC
Complicated Cyst
Mixed echogenicity
Fluid/fluid level
Floating debris
Posterior enhancement
No internal vascularity
Benign-No follow up needed

## Slide 22: CYSTS
MLO
CC
Clustered Microcysts
Multiple small cysts (< 2-3mm)
Imperceptible wall
No internal vascularity
Benign - No follow up needed
If solid component→ biopsy

## Slide 23: CALCIFICATIONS
MLO
CC
In a mass
Outside a mass
Intraductal
Calcifications appear as small echogenic foci on ultrasound.

## Slide 24: CALCIFICATIONS
MLO
CC
Large dystrophic calcifications may appear echogenic superficially (arrow head), with marked posterior shadowing (long arrow).
Dystrophic calcification on US
Dystrophic calcification on MG

## Slide 25: LYMPH NODES
MLO
CC
Eccentric cortical thickening ≥ 3mm
Attenuated to
complete loss of
fatty hilum
Normal
Maintain fatty hilum
Thin uniform cortex
Abnormal